# ColdFire Reference Card

| Mneumonic | Addressing modes | Bit Pattern | Condition Codes |
| --- | --- | --- | --- |
| ADD (L) add two values | Source + destination -> destination ADD <ea>y + Dx --> Dx; ADD Dx + <ea>y --> <ea>y Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • • Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • | 1101 Register[3] Opmode[3] EA-mode[3] EA-register[3] Opmode: 010: <ea>y + Dx --> Dx 110: Dx + <ea>y --> <ea>y | X N Z V C |
| ADDA (L) add address | Source + destination -> destination ADDA <ea>y,Ax Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • • | 1101 R[3] 111 EA-mode[3] EA-register[3] | not affected |
| ADDI (L) add immediate | Immediate Data + destination -> destination ADDI #<data>,Dx | 0000 0110 1000 0 R[3] upper word of immediate data[16] lower word of immediate data[16] | X N Z V C |
| ADDQ (L) add quick | Immediate Data + destination -> destination ADDQ #<data>,<ea>x Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • | 0101 DATA[3] 010 EA-mode[3] EA-register[3] | X N Z V C |
| ADDX (L) add with extend | Source + destination + X -> destination ADDX Dy,Dx | 1101 Register Dx[3] 11 0000 Register Dy[3] | X N Z V C |
| AND (L) logical AND | Source + destination -> destination AND Dy,<ea>x; AND <ea>y,Dx Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • | 1100 Register[3] Opmode[3] EA-mode[3] EA-register[3] Opmode: 110: AND Dy,<ea>x 010: AND <ea>y,Dx | N Z V=0 C=0 |
| ANDI (L) logical AND immediate | Immediate Data + destination -> destination ADDI #<data>,Dx | 0000 0010 1000 0 Register[3] | N Z V=0 C=0 |
| ASL, ASR arithmetic shift left and right | Destination shifted by count -> destination ASd Dy, Dx; ASd #<data>,Dx where d is direction: L or R | 1110 count register[3] dr[1] 1 0 ir[1] 00 register[3] count register: specifies shift count dr: direction: 0 shift right, 1 shift left ir: 0 immediate shift count, 1 register shift | X N Z V=0 C |
| Bcc (B,W) branch conditionally | If condtion true, then PC + dn -> PC Bcc <label>; where cc is a condition code from the condition code table | 0110 condition[4] displacement[8] or 0110 condition[4] 0000 0000 displacement[16] | not affected |
| BCHG (B,L) test bit and change | 1. (<bit number> of Destination) -> Z 2. (<bit number> of Destination) -> <bit number> of destination BCHG Dy,<ea>x; BCHG #<data>,<ea>x Destination (1 and 2) Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> L • • • • • • • L • • • • | 1. 0000 Register[3] 101 EA-mode[3] EA-register[3] 2. 0000 1000 01 EA-mode[3] EA-register[3] 0000 0000 bit number[8] | Z |
| BCLR (B,L) test bit and clear | 1. (<bit number> of Destination) -> Z 2. 0 -> <bit number> of destination BCLR Dy,<ea>x; BCLR #<data>,<ea>x Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> L • • • • • • • L • • • • | 1. 0000 Register[3] 110 EA-mode[3] EA-register[3] 2. 0000 1000 10 EA-mode[3] EA-register[3] 0000 0000 bit number[8] | Z |
| BRA (B,W) branch | PC + dn -> PC BRA <label> | 0110 0000 displacement[8] or 0110 0000 0000 0000 displacement[16] | not affected |
| BSET (B,L) test bit and set | 1.TEST (<bit number> of Destination) -> Z 2. 1 -> <bit number> of destination BSET Dy,<ea>x; BSET #<data>,<ea>x Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> L • • • • • • • L • • • • | 1. 0000 Register[3] 111 EA-mode[3] EA-register[3] 2. 0000 1000 11 EA-mode[3] EA-register[3] 0000 0000 bit number[8] | Z |
| BSR (B,W) branch to subroutine | SP - 4 -> SP; Next PC -> (SP); PC + dn -> PC BSR <label> | 0110 0001 displacement[8] or 0110 0001 0000 0000 displacement[16] | not affected |
| BTST (B,L) test bit | 1.(<bit number> of Destination) -> Z BTST Dy,<ea>x; BTST #<data>,<ea>x Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> L • • • • • • • L • • • • | 1. 0000 Register[3] 100 EA-mode[3] EA-register[3] 2. 0000 1000 00 EA-mode[3] EA-register[3] 0000 0000 bit number[8] | Z |
| CLR (B,W,L) clear | 0 -> destination Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • | 0100 0010 size[2] EA-mode[3] EA-register[3] size: 00 byte, 01 word, 10 long | N=0 Z=1 V=0 C=0 |
| CMP (L) compare | Destination - source -> cc CMP <ea>y, Dx Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • • | 1011 Register[3] 010 EA-mode[3] EA-register[3] | N Z V C |
| CMPA (L) compare address | Destination - Source -> cc CMPA <ea>y,Ax Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • • | 1011 Register[3] 111 EA-mode[3] EA-register[3] | N Z V C |
| CMPI (L) compare immediate | Destination - immediate data -> cc CMPI #<data>,Dx | 0000 1100 1000 0 Register[3] Upper word of immediate data[16] Lower word of immediate data[16] | N Z V C |
| DIVS (W,L) signed divide | Source / destination -> destination 1. DIVS.L <ea>y,Dx (32 Dx/ 32 -> 32q in Dx) 2. DIVS.W <ea>y,Dx (16 Dx/ 16 -> 16r:16q in Dx) Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • • • • • • | 1. Word 1000 Register[3] 111 Ea-mode[3] EA-register[3] 2. Long 0100 1100 01 EA-mode[3] EA-register[3] 0 Register Dx[3] 1000 0000 0 Register Dx[3] | N Z V C=0 |
| DIVU (W,L) unsigned divide | Source / destination -> destination 1. DIVU.L <ea>y,Dx (32 Dx/ 32 -> 32q in Dx) 2. DIVU.W <ea>y,Dx (16 Dx/ 16 -> 16r:16q in Dx) Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • • • • • • | 1. Word 1000 Register[3] 011 Ea-mode[3] EA-register[3] 2. Long 0100 1100 01 EA-mode[3] EA-register[3] 0 Register Dx[3] 0000 0000 0 Register Dx[3] | N Z V C=0 |
| EOR (L) logical XOR | Source XOR destination -> destination EOR Dy,<ea>x Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • | 1011 Register[3] 110 EA-mode[3] EA-register[3] | N Z V=0 C=0 |
| EORI (L) logical XOR immediate | Immediate data XOR destination -> destination EORI #<data>,Dx | 0000 1010 1000 0 Register[3] Upper word of immediate data[16] Lower word of immediate data[16] | N Z V=0 C=0 |
| EXT, EXTB (W,L) sign extend | Destination sign - extended -> destination EXT.W Dx (extend byte to word) EXT.L Dx (extend word to longword) EXTB.L Dx (extend byte to longword) | 0100 100 Opmode[3] 000 Register[3] Opmode: 010: EXT.W Dx 011: EXT.L Dx 111: EXTB.L Dx | N Z V=0 C=0 |
| JMP (unsized) jump | Target address -> PC JMP <ea>y Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • | 0100 1110 11 EA-mode[3] EA-register[3] | not affected |
| JSR (unsized) jump to subroutine | SP-4 -> SP; Next PC -> (SP); Target address -> PC Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • | 0100 1110 10 EA-mode[3] EA-register[3] | not affected |
| LEA (L) load effective address | Effective address -> destination LEA <ea>y, Ax Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • | 0100 Register[3] 111 EA-mode[3] EA-register[3] | not affected |
| LINK (W) link and allocate | SP - 4 -> SP; Ax -> (SP); SP -> Ax; SP + d16 -> SP LINK Ax,#<displacement> | 0100 1110 0101 0 Register[3] | not affected |
| LSL, LSR (L) logical shift left and right | Destination shifted by count -> destination LSd Dy,Dx; LSD #<data>,Dx (where d is direction: L or R) | 1111 count/register[3] dr[1] 10 ir[1] 01 register[3] | X N Z V=0 C |
| MOVE, MOVEA (B,W,L) move | Source -> Destination Move <ea>y,<ea>x; MOVEA <ea>y,Ax Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • • Restricted modes Source addressing mode Destination Addressing mode Dy, Ay, (Ay), (Ay)+,-(Ay) All possible (d16,Ay), (d16,PC) All except (d8,Ay,Xi), (xxx).W, (xxx).L (d8,Ay,Xi), (d8,PC,Xi), (xxx).W, xxx.(L), #<xxx> All except (d8,Ay,Xi), (d16,Ay), (xxx).W, (xxx).L | 00 Size[2] Destination-Register[3] Destination-Mode[3] Source-Mode[3] Source-Register[3] Size: 01 byte; 11 word; 10 long | N Z V=0 C=0 |
| MOVE from CCR (W) move from condition code register | CCR -> destination MOVE CCR,Dx | 0100 0010 1100 0 Register[3] | not affected |
| MOVE to CCR (W) move to condition code register | Source -> CCR MOVE Dy,CCR; MOVE #<data>,CCR Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • | 0100 0100 11 EA-mode[3] EA-register[3] | X N Z V C |
| MOVEM (L) move multiple registers | Registers -> destination or Source -> Registers MOVEM <list>,<ea>x; MOVEM <ea>y,<list> Register to Memory or Memory to Register Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • | 0100 1 dr[1] 0011 EA-mode[3] EA-register[3] registers to transfer/modify bit mask[16] dr: 0 register to memory; 1 memory to register | not affected |
| MOVEQ (L) move quick | Immediate data -> destination MOVEQ #<data>,Dx | 0111 Register[3] 0 Data[8] Data is 8 bits, sign-extended to a long | N Z V=0 C=0 |
| MULS (W,L) signed multiply | Source x destination -> destination 1. MULS.L <ea>y,Dx (32 x 32 -> 32) 2. MULS.W <ea>y,Dx (16 x 16 -> 32) Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • • • • • • | 1. Word 1100 Register[3] 111 Ea-mode[3] EA-register[3] 2. Long 0100 1100 00 EA-mode[3] EA-register[3] 0 Register Dx[3] 1000 0000 0000 | N Z V=0 C=0 |
| MULU (W,L) unsigned multiply | Source x destination -> destination 1. MULU.L <ea>y,Dx (32 x 32 -> 32) 2. MULU.W <ea>y,Dx (16 x 16 -> 32) Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • • • • • • | 1. Word 1100 Register[3] 011 Ea-mode[3] EA-register[3] 2. Long 0100 1100 00 EA-mode[3] EA-register[3] 0 Register Dx[3] 0000 0000 0000 | N Z V=0 C=0 |
| NEG (L) negate | 0 - destination -> destination NEG Dx | 0100 0100 1000 0 Register[3] | X N Z V C |
| NEGX (L) negate with extend | 0 - destination - X -> destination NEGX Dx | 0100 0000 1000 0 Register[3] | X N Z V C |
| NOP (unsized) no operation | No operation NOP | 0100 1110 0111 0001 = $4E71 | not affected |
| NOT (L) logical complement | ~ destination -> destination NOT Dx | 0100 0110 1000 0 Register[3] | N Z V=0 C=0 |
| OR (L) logical inclusive-OR | Source OR destination -> destination OR Dy,<ea>x; OR <ea>y,Dy Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • | 1000 Register[3] Opmode[3] EA-mode[3] EA-register[3] Opmode: 110: OR Dy,<ea>x 010: OR <ea>y,Dy | N Z V=0 C=0 |
| ORI (L) logical inclusive-OR immediate | Immediate data OR destination -> destination ORI #<data>,Dx | 0000 0000 1000 0 Register[3] Upper word of immediate data[16] Lower word of immediate data[16] | N Z V=0 C=0 |
| PEA (L) push effective address onto stack | SP - 4 -> SP; <ea>y -> (SP) PEA <ea>y Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • | 0100 1000 01 EA-mode[3] EA-register[3] | not affected |
| REMS (L) signed divide remainder (if Dw=Dx then DIVU is executed instead) | Destination / Source -> Remainder 1. REMU.L <ea>y,Dw:Dx (32 Dx/ 32 -> 32r in Dw) Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • | Long 0100 1100 01 EA-mode[3] EA-register[3] 0 Register Dx[3] 1000 0000 0 Register Dw[3] | N Z V C=0 |
| REMU (L) unsigned divide remainder (if Dw=Dx then DIVU is executed instead) | Destination / Source -> Remainder 1. REMU.L <ea>y,Dw:Dx (32 Dx/ 32 -> 32r in Dw) Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • | Long 0100 1100 01 EA-mode[3] EA-register[3] 0 Register Dx[3] 0000 0000 0 Register Dw[3] | N Z V C=0 |
| RTS (unsized) return from subroutine | (SP) -> PC; SP + 4 -> SP RTS | 0100 1110 0111 0101 = $4E75 | not affected |
| SUB (L) subtract | Destination - source -> destination SUB Dy,<ea>x; SUB <ea>y,DY Source Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • • Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • | 1001 Register[3] Opmode[3] EA-mode[3] EA-register[3] Opmode: 010: SUB Dy,<ea>x 110: SUB <ea>y,DY | X N Z V C |
| SUBA (L) subtract address | Destination - source -> destination SUBA <ea>y,Ax Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • • | 1001 Register[3] 111 EA-mode[3] EA-register[3] | not affected |
| SUBI (L) subtract immediate | Destination - immediate data -> destination SUBI #<data>,Dx | 0000 0100 1000 0 Register[3] Upper word of immediate data[16] Lower word of immediate data[16] | X N Z V C |
| SUBQ (L) subtract quick | Destination - immediate data -> destination SUBQ #<data>,<ea>x Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • | 0101 data[3] 110 EA-mode[3] EA-register[3] | X N Z V C |
| SUBX (L) subtract with extend | Destination - source -> destination SUBX Dy,Dx | 1001 Dx[3] 1 1000 0 Dy[3] | X N Z V C |
| Scc (B) set according to condition | If condition true then 1s -> destination else 0s -> destination Scc Dx (cc is condition code, see condition codes table) | 0101 Condtion[3] 1100 0 Register[3] | not affected |
| SWAP (W) swap register words | Register bits 31 to 16 <--> Register bits 15 to 0 SWAP Dx | 0100 1000 0100 0 Register[3] | N Z V=0 C=0 |
| TRAP (unsized) trap | TRAP #<vector> | 0100 1110 0100 Vector[4] | not affected |
| TST (B,W,L) test operand | Destination tested -> condition codes TST <ea>y Destination Dn An (An) (An)+ -(An) (d16,An) (d8,An,Xi) (d16,PC) (d8,PC,Xi) (xxx).W (xxx).L #<xxx> • • • • • • • • • • • • | 0100 1010 Size[2] EA-mode[3] EA-register[3] | N Z V=0 C=0 |
| UNLK (unsized) unlink | Ax -> SP; (SP) -> Ax; SP+4 -> SP UNLK Ax | 0100 1110 0101 1 Register[3] | not affected |

## Effective Addressing Modes

| Addressing Modes | Syntax | Mode Field | Register Field |
| --- | --- | --- | --- |
| Data Register Direct | Dn | 000 | register number |
| Address Register Direct | An | 001 | register number |
| Address Register Indirect | (An) | 010 | register number |
| Postincrement Address Register Indirect | (An)+ | 011 | register number |
| Predecrement Address Register Indirect | -(An) | 100 | register number |
| 8-bit index displacement Address Register Indirect | (d8,An,Xi) | 110 | register number |
| Program counter indirect with displacement | (d16,PC) | 111 | 010 |
| Program counter indirect with index 8-bit displacement | (d8,PC,Xi) | 111 | 011 |
| Absolute Short | (xxx).W | 111 | 000 |
| Absolute Long | (xxx).L | 111 | 001 |
| Immediate | #<xxx> | 111 | 100 |

## Condition Codes Register

The CCR is the least significant byte of the status register (SR). Bits 4-0 are the condition code flags:

- X: Extend condition code (bit 4)

- N: Negative condition code (bit 3)

- Z: Zero condition code (bit 2)

- V: Overflow condition code (bit 1)

- C: Carry condition code (bit 0)

## Condition Codes Table

| Mnemonic | Condition | Encoding | Test |
| --- | --- | --- | --- |
| T (BRA) | True | 0000 | 1 |
| F (BSR) | False | 0001 | 0 |
| HI | High | 0010 | C' * Z' |
| LS | Lower or Same | 0011 | C + Z |
| CC (HI) | Carry Clear | 0100 | C' |
| CS (LO) | Carry Set | 0101 | C |
| NE | Not Equal | 0110 | Z' |
| EQ | Equal | 0111 | Z |
| VC | Overflow Clear | 1000 | V' |
| VS | Overflow Set | 1001 | V |
| PL | Plus | 1010 | N' |
| MI | Minus | 1011 | N |
| GE | Greater or Equal | 1100 | N * V + N' * V' |
| LT | Less Than | 1101 | N * V' + N' * V |
| GT | Greater Than | 1110 | N * V * Z' + N' * V' * Z' |
| LE | Less or Equal | 1111 | Z + N * V' + N' * V |
| A prime, ' indicates the complement. |
| A plus, + indicates an or operation. |
| A star, * indicates an and operation. |

## ASCII Chart

0   1   2   3   4   5   6   7   8   9   A   B   C   D   E   F

0  NUL SOH STX ETX EOT ENQ ACK BEL BS  HT  LF  VT  FF  CR  SO  SI

1  DLE DC1 DC2 DC3 DC4 NAK SYN ETB CAN EM  SUB ESC FS  GS  RS  US

2   SP  !   "   #   $   %   &   '   (   )   *   +   ,   -   .   /

3   0   1   2   3   4   5   6   7   8   9   :   ;   <   =   >   ?

4   @   A   B   C   D   E   F   G   H   I   J   K   L   M   N   O

5   P   Q   R   S   T   U   V   W   X   Y   Z   [   \   ]   ^   _

6   `   a   b   c   d   e   f   g   h   i   j   k   l   m   n   o

7   p   q   r   s   t   u   v   w   x   y   z   {   |   }   ~ DEL

## Notes

Supervisor (privileged) instructions not included in chart.
While we have tried to be accurate, there are no guarantees that this chart is completely correct. If you find an error, please send mail to Roger.

Developed and produced by Ashish Mishra, E&CE Dept., U of W, 1999. Updated E. Praetzel 2004

Added DIVU, DIVS, REMS, REMU for 5307 processor. The V4 processors add a lot more.